Precision Devices INC. – 8840N. Greenview Drive, Middleton WI 53562, Tel- 1-800-274-XTAL, Fax- 1-608-831-3343,

www.pdixtal.com  Outside US Phone- 608-381-4445, E-mail- sales@pdixtal.com

PD (HK) Ltd. – Tel- (852)-2367-3626, Fax- (852)-2646-3122, E-mail- sales@pdixtal.com.hk

PD (UK) Ltd. – Tel- +44 (0)1223 834444, Fax- +44(0)1223 834589, E-mail- sales@pdixtal.co.uk

# Text boxes

VOLTAGE CONTROLLED CRYSTAL OSCILLATOR (VCXO)

### VC29-3

The VC29-3 series provides a range of voltage controlled crystal oscillators operating at +3.3V supply with a HCMOS/TTL compatible output.  The control voltage range of (100ppm minimum ensures an absolute pull range of at least (50ppm with a typical linearity of (3%.

## ADVANTAGES

Surface Mount Package

Cost Effective

Wide Operating Frequency

Wide Frequency Adjustment Range

## APPLICATIONS

(Telecommunications

(Portable Instrumentation

(Synthesizers.

(Phase Locked Loops.

| PARAMETER | MINIMUM | MAXIMUM | UNITS |
| --- | --- | --- | --- |
| NOMINAL FREQUENCY (Fo) | 4.0 | 100 | MHz |
| CALIBRATION TOLERANCE (With +1.65V on pin 1) | -10 | +10 | ppm |
| FREQUENCY STABILITY Over Temperature Range (See Note 2) Ageing (per year at +25C) Over Supply Voltage Variation (Vcc = +3.3V ±5.0%) | -25 -2.0 -5.0 | +25 +2.0 +5.0 | ppm |
| OPERATING TEMPERATURE RANGE (See Note 2) | -20 | +70 | C |
| STORAGE TEMPERATURE RANGE | -40 | +85 | C |
| SUPPLY VOLTAGE (Vcc) (See Note 2) | +3.135 | +3.465 | V |
| SUPPLY CURRENT (Dependant upon nominal frequency) | 5.0 | 25.0 | mA |
| OUTPUT WAVEFORM HCMOS/TTL Logic Levels Duty Cycle (@ Vcc/2) Fall and rise times | 0.1Vcc 40 3 | 0.9Vcc 60 10 | V % ns |
| Voltage Control Range +1.65V (1.5V (Positive polarity) | (100 | (200 | ppm |
| Linearity |  | (10 | % |
| Input Impedance | 50,000 |  | ( |
| Modulation Bandwidth | 10 |  | kHz |

ELECTRICAL PERFORMANCE  (Ta=25°c, CL = 10k//10pF and Vcc = +3.3V)

NOTES   1) To order, state part number and nominal frequency e.g. VC29-3 32.768MHz

2) Other temperature ranges, stabilities and supply voltages are readily available upon request.

| Parameter | Standard Observed |
| --- | --- |
| Mechanical Shock | MIL-STD-202 Method 213, Condition C |
| Vibration | MIL-STD-202 Method 201, 204, and 214 |
| Solderability | IPC/EIA-STD-002A |