| PARAMETER | MINIMUM | MAXIMUM | UNITS |
| --- | --- | --- | --- |
| Center Frequency |  |  | MHz |
| Oscillation Mode Fundamental |  |  |  |
| Maximum Series Resistance (See Note 4) |  |  | Ohms |
| Frequency Stability at +25°C (See Note 2) ±50.0ppm Typ. |  |  | ppm |
| Frequency Stability Over Temperature ±50.0ppm Typ. |  |  | ppm |
| Operating Temperature Range (See Note 2) |  |  | °C |
| Storage Temperature Range |  |  | °C |
| Drive Level 100.0uW Typical |  |  |  |
| Seal Method Resistance Weld |  |  |  |
| Shunt Capacitance |  |  | pF |
| Motional Capacitance | Customer Request |  |
| Load Capacitance |  |  | pF |
| Aging per year |  |  | ppm |

| Parameter | Standard Observed |
| --- | --- |
| Mechanical Shock | MIL-STD-202 Method 213, Condition C |
| Vibration | MIL-STD-202 Method 201, 204, and 214 |
| Hermeticity | MIL-STD-202, Method 112 |
| Solderability | IPC/EIA-STD-002A |

Precision Devices INC. – 8840N. Greenview Drive, Middleton WI 53562, Tel- 1-800-274-XTAL, Fax- 1-608-831-3343,

www.pdixtal.com  Outside US Phone- 608-381-4445, E-mail- sales@pdixtal.com

PD (HK) Ltd. – Tel- (852)-2367-3626, Fax- (852)-2646-3122, E-mail- sales@pdixtal.com.hk

PD (UK) Ltd. – Tel- +44 (0)1223 834444, Fax- +44(0)1223 834589, E-mail- sales@pdixtal.co.uk

# Text boxes

PLASTIC QUARTZ CRYSTAL OSCILLATOR

### OP9

The OP9 package

## ADVANTAGES

Surface Mount

Low Cost

Hermetic Package

70MHz Operating Frequency

## APPLICATIONS

Telecommunications

Avionics

Microprocessors

Personal Computers

ELECTRICAL PERFORMANCE (Ta=25°c)

NOTES   1) To order, state part number, options and nominal frequency e.g. OP9 100.000MHz

2) Other temperature ranges, stabilities and electrical parameters are readily available upon request.

3) Other specifications available upon request.

4) Dependent on frequency and mode