| PARAMETER | MINIMUM | MAXIMUM | UNITS |
| --- | --- | --- | --- |
| Center Frequency | 100.0KHz | 80.0MHz |  |
| Frequency Tolerance @ +23°C ±1°C | ±15.0 | ±25.0 | ppm |
| Operating Temperature Range | -55 | +125 | °C |
| Frequency Stability | ±25 | ±100 | ppm |
| Storage Temperature Range | -62 | +125 | °C |
| Duty Cycle @ 1.4V | 45 | 55 | % |
| Rise Fall Times 2.0nS Typ. |  | 5.0 | nS |
| Supply Current over Temperature | 30 | 158 | mA |
| Supply Voltage | +4.75 | +5.25 | Vdc |
| Output: TTL/CMOS |  | 10TTL |  |
| Aging: ±0.7ppm for 30 Days, ±1.5ppm for 90 Days | ±0.7 | ±5.0 | ppm/year |
| Load Max. 10.0TTL (A TTL unit is defined as 1.6mA Sink, 0.4mA Source, 2.0pF) |

| Parameter | Standard Observed |
| --- | --- |
| Mechanical Shock | MIL-STD-202 Method 213, Condition C |
| Vibration | MIL-STD-202 Method 201, 204, and 214 |
| Hermeticity | MIL-STD-202, Method 112 |
| Solderability | IPC/EIA-STD-002A |

Precision Devices INC. – 8840N. Greenview Drive, Middleton WI 53562, Tel- 1-800-274-XTAL, Fax- 1-608-831-3343,

www.pdixtal.com  Outside US Phone- 608-381-4445, E-mail- sales@pdixtal.com

PD (HK) Ltd. – Tel- (852)-2367-3626, Fax- (852)-2646-3122, E-mail- sales@pdixtal.com.hk

PD (UK) Ltd. – Tel- +44 (0)1223 834444, Fax- +44(0)1223 834589, E-mail- sales@pdixtal.co.uk

# Text boxes

MIL-PRF-55310/16H

### QPL

Military Certificates:

MIL-STD-790: Product Assurance

MIL-PRF-38534: Hybrid Microcircuit Certification

MIL-Laboratory Suitability

## ADVANTAGES

Full Military Approval

High Shock and Vibration

Extended Temperature Range

Double Hermetic Seal

## APPLICATIONS

Aircraft

Missile

Two Way Radio

Computer

ELECTRICAL PERFORMANCE (Ta=23°c)

NOTES    1) To order, state part number, options and nominal frequency e.g. 14-Pin Dip 78.000MHz

2) Other temperature ranges, stabilities and electrical parameters are readily available upon request.

3) Other specifications available upon request.