| Parameter | Standard Observed |
| --- | --- |
| Mechanical Shock | MIL-STD-202 Method 213, Condition C |
| Vibration | MIL-STD-202 Method 201, 204, and 214 |
| Solderability | IPC/EIA-STD-002A |

Precision Devices INC. – 8840N. Greenview Drive, Middleton WI 53562, Tel- 1-800-274-XTAL, Fax- 1-608-831-3343,

www.pdixtal.com  Outside US Phone- 608-381-4445, E-mail- sales@pdixtal.com

PD (HK) Ltd. – Tel- (852)-2367-3626, Fax- (852)-2646-3122, E-mail- sales@pdixtal.com.hk

PD (UK) Ltd. – Tel- +44 (0)1223 834444, Fax- +44(0)1223 834589, E-mail- sales@pdixtal.co.uk

# Text boxes

S.M.D. TEMPERATURE COMPENSATED CRYSTAL OSCILLATOR (TCXO)

### TC26-5

The TC26-5 series provides a range of temperature compensated crystal oscillators operating at +5.0V supply with either HCMOS or clipped sinewave outputs. The optional voltage control feature and flexible design makes this range of TCXO’s an ideal choice for existing and future applications where reliability, cost and performance are critical factors.

## ADVANTAGES

Surface Mount

Extended Temperature Range

Optional Output and Adjust Method.

Wide Operating Frequency Range

## APPLICATIONS

Telecommunications

Portable Instrumentation

Mobile Communications.

Global Positioning Systems (GPS)

| PARAMETER | MINIMUM | MAXIMUM | UNITS |
| --- | --- | --- | --- |
| NOMINAL FREQUENCY (Fo) | 8.0 | 100 | MHz |
| CALIBRATION TOLERANCE | -1.0 | +1.0 | ppm |
| FREQUENCY STABILITY Over Temperature Range (See Note 2) Ageing (per year at +25C) Over Supply Voltage Variation (Vcc = +5.0V ±5.0%) | -2.5 -1.0 -0.3 | +2.5 +1.0 +0.3 | ppm |
| OPERATING TEMPERATURE RANGE (See Note 2) | -40 | +85 | C |
| STORAGE TEMPERATURE RANGE | -55 | +105 | C |
| SUPPLY VOLTAGE (Vcc) (See Note 2) | +4.75 | +5.25 | V |
| SUPPLY CURRENT (Dependant upon nominal frequency) | 2.0 | 15.0 | mA |
| OUTPUT WAVEFORM HCMOS/TTL (Order code TC26-5A) Logic Levels Duty Cycle (@ Vcc/2) Fall and rise times | 0.1Vcc 40 3 | 0.9Vcc 60 10 | V % ns |
| OUTPUT WAVEFORM Clipped sinewave (Order code TC26-5B) Peak to Peak amplitude | 1.0 |  | V |
| FREQUENCY ADJUSTMENT (Internal trimmer) | ±3 |  | ppm |
| VOLTAGE CONTROL +2.5V ±2.0V (Add suffix V to order code) | ±5 |  | ppm |

ELECTRICAL PERFORMANCE  (Ta=25°c, CL = 10k//10pF and Vcc = +5.0V)

NOTES   1) To order, state part number, options and nominal frequency e.g. TC26-5AV 10.000MHz

2) Other temperature ranges, stabilities and supply voltages are readily available upon request.

3) Other Specifications Available upon request